Lab 1 Answer Key

Q1: Comment on the differences between the residual error and RMSE derived using each of the transformation types. Explain the effect of higher-order transformations on rectification of the Turkey Lakes DEM. (4 marks)

Increasing the polynomial order lowers the individual residuals and the RMSE of the transformation. 1st order RMSE = 14.131 m, 2nd order RMSE = 11.207 m, 3rd order RMSE = 6.49 m (if all points are included). This is a fairly significant reduction. It is caused by the increased warping of the transformation plane…

Q2: Print the equation document and hand it in with the written component of your assignment (1 mark).

These are the results of my GCPs and transformation:

Image Rectification

Transformation Type: Third-order Polynomial

Equation Form:

X' = a0 + a1X + a2Y + a3X^2 + a4XY + a5Y^2 + a6X^3 + a7X^2Y + a8XY^2 + a9Y^3

Y' = b0 + b1X + b2Y + b3X^2 + b4XY + b5Y^2 + b6X^3 + b7X^2Y + b8XY^2 + b9Y^3

a			b

0	-1.91846987116288E-08	-9.82143314268542E-07

1	5.05707557183419E-03	4.49901554812963E-05

2	-2.95829315449411E-04	6.1091786940722E-04

3	1.05159065803907E-04	3.31061894986482E-05

4	-3.52927318234355E-05	-3.34060950365148E-06

5	-5.85214394051776E-05	-8.96521033961715E-06

6	5.02129395080323E-04	1.02614959742744E-05

7	-1.80695077143172E-04	-4.22797450485235E-05

8	-2.55468078715857E-04	4.02375912567385E-05

9	-8.49467322117296E-05	2.78579333375444E-05

Note: coefficients have been standardized

# of GCPs used:		17

Min. # of GCPs:		10

Recommended # of GCPs:	at least 20 to 30

# Image X		Image Y		 Target X	Target Y		Residual

4531.3691	684.4443	698380		5212425		0.504

4356.5091	3482.2043	698000		5215200		not used

3662.0611	2058.3443	697420		5213720		4.477

1823.5371	3402.2683	695500		5214950		2.066

5150.8731	4906.0643	698700		5216700		0.078

1104.1131	1179.0483	694925		5212700		0.573

2512.9851	5270.7723	696050		5216850		0.715

2318.1411	764.3803	696170		5212320		2.562

5290.7611	2278.1683	699075		5214100		0.557

2737.7186	2193.1724	696500		5213800		not used

2442.9642	1333.8884	696250		5212910		3.051

4311.4072	3746.8776	697960		5215460		4.682

3467.1108	1528.7261	697250		5213180		6.847

1029.1424	4616.1532	694610		5216100		0.406

2427.9767	3032.4729	696130		5214620		4.032

1438.801	2427.9767	695170		5213940		not used

3756.8693	2008.3264	697520		5213680		3.502

3492.04	2402.9975	697230	5214060	4.945

2962.5313	3831.8068	696600	5215440	5.268

4541.2157	3572.0233	698200	5215300	4.222

RMSE:	2.852

Q3: How has rectification changed ‘DEM XY’? Examine the rectified image’s file attributes (file menu ==> ‘File Attributes’). What are the minimum and maximum X and Y values? Are these bounds what you would expect? (3 marks)

A3: The transformation has rotated the DEM counter-clockwise (about 10 to 15 degrees) and warped it very slightly.

(Their min and max X and Y will be slightly different depending on their GCPs)

Min X: 693558.744311908

Max X: 699657.494730778

Min Y: 5211708.94324397

Max Y: 5217254.00181861

Looking at the OBM map, these values appear to be reasonable.

Q4: Define Root Mean Square Error. In the process of map rectification, what is the threshold in RMSE that they GIS analyst attempts to stay below? How did your rectification compare to this threshold? Suggest some ways that you could have improved the accuracy of the rectification (5 marks)

A4: they could give you a mathematical definition or perhaps a general description of how it is a measure of the overall or average error magnitude in the transformation. The grid resolution sets the threshold in RMSE. In this case that is 5 meters. My RMSE of 2.852 m was well below that…a third-order can do that! To improve the accuracy of the rectification, they could have:

- Included more GCP points

- Attained a better spread of points

- Measured the map coordinates more precisely than was possible with the ‘Very expensive, high precision map reading tool’

- Got a smaller-scale map

Q5: Comment on the distribution of your GCP points (only the ones that were used in the final equation). That is, where is the distribution of GCPs adequate and where is it not? (2 marks)

A5: I think that most people will have a hard time finding points in the north central part of the DEM (i.e. Batch mountain area). There are plenty of points to pick from in the southern portion.

Q6: What coordinate system is used for the Earth’s spheroid? In the transformation of the Earth from a spheroid to a flat map, what geometric properties of the map may be altered? What projection and coordinate system are commonly used for maps of the Earth’s topography? (3 marks)

A6. Lat/long or geographic coordinates. Angles, areas, distances, directions. UTM.

Q7: Which resampling methods is more appropriate for transforming discrete entity data and why? (2 marks)

A7. Nearest neighbour because the values in the resulting map are the same as those of the original image. Therefore, the values near edges of polygons are preserved. Using bilinear interpolation, edges are average values, which simply don’t make sense.

Q8: How has the datum transformation affected the elevations of the DEM? What about the minimum and maximum X and Y coordinates? Explain why these changes have occurred. (3 marks)

The datum transformation has raised elevations in the DEM by about 30 m. The x-coordinates have not been significantly altered but there has been a shift in the y-coordinates of about 220 m to the south. This is the effect of re-projecting the DEM from a WGS ellipsoid onto a Clarke 66 ellipsoid, which have different dimensions.